## Slide 1: Human Factors Analysis of Automated Planning Technologies for Human-Robot Teaming
Vignesh Narayanan
Master of Science – Thesis Defense
Graduate Supervisory Committee
Dr. Subbarao Kambhampati, Co-Chair
Dr. Yu Zhang, Co-Chair
Dr. Nancy Cooke
Dr. Georgios Fainekos

## Slide 2: Current state of Human-Robot Teams (HRT)
The robotic capabilities in many domains are still insufficient to execute several tasks robustly and efficiently.
  Mostly remotely controlled
  In restricted settings (manufacturing)
  And programmed for specific assistance
Robots can still accomplish those tasks as a team with human assistance.
Notes: The vision of humans and robots working together to accomplish complex team tasks is driving much of the current research in the area of autonomous teamwork. As robots become more capable they can handle increasingly complex tasks and highly uncertain environments, but the current robotic capabilities in many domains are still insufficient to execute these tasks robustly and efficiently. In these scenarios, robots can still accomplish the tasks with human assistance as human capabilities are often better suited for some tasks and they complement robot capabilities in many situations. Thus, for robots to become an integral part of society, human-robot teams must be effective in a variety of settings.

## Slide 3: Lessons from Human-Human Teams *
  Planning - Agents mostly plan for themselves
  Proactive Support – Often no need to specifically ask for help
    Higher teaming performance
Connections to Automated Planning Technologies
* “Communication Between Teammates in Urban Search and Rescue”, Cade Earl Bartlett, Nancy Cooke

## Slide 4: Automated Planning Technologies in Human-Robot Teams
To move closer to human-human teams we need automated planning technologies.
  Automated planning system:
    Enables autonomy
    Allows the robot agent to reason directly about goal (like human counterparts)
    Supports high level (task or sub-task) decision making beyond low level motion commands.
However
  Planning - Agents mostly plan for themselves
  Proactive Support – Often no need to specifically ask for help
    ? Higher teaming performance
  Apart from positive effects, automation can have negative influence on human performance too:
    Trust factor
    Loss of Situation Awareness

## Slide 5: Overview of my Thesis
STUDY 1 *
Is automated planning for robot preferred in Human-Robot teams?
STUDY 2 **
Is proactive support from robot preferred in Human-Robot teams?
* “Automated Planning for Peer-to-peer Teaming and its Evaluation in Remote Human-Robot Interaction ” Vignesh Narayanan, Yu Zhang, Nathaniel Mendoza and Subbarao Kambhampati. 10th ACM/IEEE Intl. Conf on Human Robot Interaction (HRI), 2015.
** “A Human Factors Analysis of Proactive Assistance in Human-robot Teaming” Yu (Tony) Zhang, Vignesh Narayanan, Tathagata Chakraborty & Subbarao Kambhampati. IROS 2015.

## Slide 6: Types of Human-Robot Teams
Human Robot Teaming
Remote
Proximal
Based on physical distance between Human and Robot

## Slide 7: STUDY 1 *
Is automated planning for robot preferred in Human-Robot teams?
* “Automated Planning for Peer-to-peer Teaming and its Evaluation in Remote Human-Robot Interaction ” Vignesh Narayanan, Yu Zhang, Nathaniel Mendoza and Subbarao Kambhampati. 10th ACM/IEEE Intl. Conf on Human Robot Interaction (HRI), 2015.

## Slide 8: Supervised Vs. Peer-to-Peer(P2P) HRT
In supervised human-robot interaction the human creates the plan for the robot to achieve the global goal.
In peer-to-peer(P2P) human-robot interaction, general planning capability is incorporated into the robot.
Notes:   Human then either directly provides motion commands or breaks the plan into sub-plans (or sub-goals) for the robot to handle.
  During plan execution, the human can interact with the robot using a low level motion controller, or a high level task and plan manager.
  The human and robot share the same global goal and collaborate to achieve it.
  An autonomous robot here can achieve the global goal alone when the task information is completely specified.

## Slide 9: Is automated planning for robot preferred in Human-Robot teams?

## Slide 10: Why not?
The trust factor –
  Are humans comfortable with robots having a planning ability ?
Information asymmetry –
  Can task information be fully specified a priori ?
  Is the knowledge always synchronized between human and robot ?
Can Automated Planning reduce effectiveness of HRTs?
Notes: Task information often cannot be completely specified in real-world applications.
Is it always bad ?
  Dynamic environmental influences
  Practicality issues
  Certain task updates require manual processing, which is prone to interpretation delay (e.g., environment changes that can only be perceived and interpreted by humans)
  The knowledge cannot be easily incorporated into the planning model (e.g., inferencing and image processing capabilities of humans)
  NO! (e.g., the human does not need to know how many rooms the robot travels through to move to a specified location).

## Slide 11
Human factors analysis to validate effectiveness of Automated Planning in human-robot teams.

## Slide 12: Urban Search And Rescue (USAR) Scenario Setup
Notes: Remote human-robot interaction
Incomplete task information – environmental changes due to disasters
Deployed during early phases of emergency response
  To explore disaster scene
  To provide real-time information
  Situation assessment to aid emergency management
Apart from human robot interaction, human also need to collaborate with other operators and related personnel.

## Slide 13: The Setup
Team goal – Report the number of casualties in as many rooms as possible, given a certain amount of time.
Incomplete task information
    Blocked doors (Information provided to subjects but not modelled by the robot inside the environment)
The subjects must also process and analyze information from the robot teammate and other sources
    Simulated by making the subjects solve puzzle problems
USAR task details

## Slide 14: The Setup
Interaction Interface

## Slide 15: Automated Planner Component
An automated planner [1] allows an automated agent to reason directly about the global goal (with the limitation coming only from the completeness assumption).
A task can be compiled into a problem instance (specified using PDDL) for an automated planner.
The planner creates a plan by connecting initial state to the goal state using the agent actions.
[1] Talamadupula, K.; Benton, J.; Kambhampati, S.; Schermerhorn, P.; and Scheutz, M. 2010. Planning for human-robot teaming in open worlds. ACM Transactions on Intelligent Systems and Technology (TIST) 1(2):14.
Notes: Various types of incompleteness like
  Partial satisfaction of the goal
  Incomplete initial state
  Incomplete action models
  Incomplete preference of the human teammate
  can also be considered in an automated planner.

## Slide 16: Evaluation Criterion
Robot with and without planning ability.
– Hypothesis 1 –
Robot with a planning capability reduces human teammate's mental workload; on the other hand, it also reduces situation awareness.
– Hypothesis 2 –
Robot with a planning capability enables more effective teaming (e.g. Gradually reduced interaction)
Hypothesis for effectiveness of Automated Planning in HRTs

## Slide 17
Objective Performance
Primary Task Performance
Secondary Task Performance
RAD & Fan-out
Skipped actions
Time Spent
Secondary Task accuracy
We use P2P-NI as a baseline
Percentage of participants time dedicated to Human-robot interaction
Humans interacted more as time ran out to improve performance
Max #robots a human can simultaneously interact with
#rooms reported in 20 mins
Mental Workload indicator

## Slide 20: Subjective Likert Scale Questionnaire

## Slide 21
Subjective Performance
Mental Workload
Situation Awareness
Complacency
Ease of working with robot
Participants workload to interact with the robot
Awareness of robot’s position
Understanding of robot actions during the task
Comfort and ease of teaming
INCONSISTENT WITH H1
INCONSISTENT WITH H1
CONSISTENT WITH H2

## Slide 22
Subjective Performance
Immediacy
Likability
Trust
How useful the participant felt about interaction
How useful the participant felt about robot as a teammate
Ease and comfort
Interaction between participant and robot was effective ?
How much the participant felt like working in a real team
Effectiveness
Perceived effectiveness
Robot sometimes performed unexpectedly ?
Robot took initiatives to achieve the common goal ?
CONSISTENT WITH H2
Improvability
How much the robot could be improved ?

## Slide 24: Summary of Study 1 *
Results are partially consistent with the hypotheses.
Subjects seemed to prefer to engage in peer-to-peer teaming.
  Task performance was higher in peer-to-peer teaming than supervised teaming.
  Peer-to-peer teaming may not reduce mental workload in short-term tasks.
  Situational awareness is not reduced significantly in peer-to-peer teaming
Generally positive attitude towards peer-to-peer team
* “Automated Planning for Peer-to-peer Teaming and its Evaluation in Remote Human-Robot Interaction ” Vignesh Narayanan, Yu Zhang, Nathaniel Mendoza and Subbarao Kambhampati. 10th ACM/IEEE Intl. Conf on Human Robot Interaction (HRI), 2015.
Notes:   Working with a proactive teammate may require more interactions at the beginning and once a mutual understanding is established, the mental workload may be reduced.
  This suggests that providing “recommended actions" may also be used as a way to reduce the negative influence of automation.

## Slide 25: STUDY 2 *
Is proactive support from robot preferred in Human-Robot teams?
* “A Human Factors Analysis of Proactive Assistance in Human-robot Teaming” Yu (Tony) Zhang, Vignesh Narayanan, Tathagata Chakraborty & Subbarao Kambhampati. IROS 2015.

## Slide 26: Active vs. Proactive support
Humans + Robots sharing workspace
  Active support – Robots can provide specific assistance when the human needs/asks for it.
  Proactive support (PS) – Assistive robots can infer the goals and intents of the humans, and take proactive actions to help them achieve their goals.

## Slide 27
Is proactive support from robot preferred in Human-Robot teams?

## Slide 28: Why not?
The trust factor –
  Are humans are comfortable with robots having a goal and intent recognition (GIR) ability ?
Being on the same page –
  Misinterpretations, delays, redundancy?
Cognitive overload –
  The human needs to replan constantly with proactive support.
Can Proactive Support reduce effectiveness of HRTs?

## Slide 29
Human factors analysis to validate effectiveness of Proactive Support in human-robot teams.

## Slide 30: The Setup
Urban Search and Rescue (USAR)

## Slide 31: The Setup
Human’s point of view

## Slide 32: The Setup
USAR environment details
Medical kits
CCTV cameras
Casualty (lightly injured)
Casualty (critically injured)
Treat casualties in medical rooms (M)
Search for casualties in rooms (R)
Fetch medical kits from storage rooms (S)

## Slide 33: The Setup
Team goal – Find and treat all casualties
  Critically injured casualties must be treated first
  Human/Robot can carry one medkit/casualty at a time
  The triage can only be performed by the human
    Simulated by making the subjects solve puzzle problems
  A medical room can only accommodate one casualty and each medical kit can be used towards one casualty.
USAR task details

## Slide 34: Action Selection (Human)
Modes of interaction between human and robot
Move
Lift/Lay down Casualty
Open Door
Conduct Triage
Grab/Drop Medkit
Goal
Inform
Request
Goal/Action updates
Stop current plan
Undo current plan
Inform current goal

## Slide 35: Action Selection (Robot)
Without PS (no GIR component)
Candidate
Goal Set
Automated Planning Component
Goal
Actions
Actions
Plan
Human
Robot
Environment
Team Utility
Assign goal to self to maximize team utility
update
Grab/Drop Medkit
Move
Carry/Lay Down Casualty
Open Door

## Slide 36: Action Selection (Robot)
Components of Proactive Support
Goal/Intent Recognition (GIR) Component
Candidate Goal Distribution
Automated Planning Component
Goal
Actions
Actions
Plan
Human
Robot
Environment
Team Utility
Assign goal to self to maximize team utility
Most probable goal of human
update
observations
Grab/Drop Medkit
Move
Carry/Lay Down Casualty
Open Door

## Slide 37: Components of Proactive Support
Automated Planning Component[1]
  Computes a plan i.e. a sequence of actions that transforms the current world state to the goal state
Intent/Goal Recognition Component[2]
  Computes a probability distribution over a set of goals depending on their likelihood given some observations
Off-the-shelf software for both modules
Automated Planning and Intent Recognition
[1] Talamadupula, K.; Benton, J.; Kambhampati, S.; Schermerhorn, P.; and Scheutz, M. 2010. Planning for human-robot teaming in open worlds. ACM Transactions on Intelligent Systems and Technology (TIST) 1(2):14.
[2] Miquel Ramirez and Hector Geffner. “Probabilistic plan recognition using off-the-shelf classical planners”. In Proceedings of the Twenty- Fourth AAAI Conference on Artificial Intelligence, AAAI 2010, Atlanta, Georgia, USA, July 11-15, 2010, 2010.

## Slide 38: Use Case
How the robot provides proactive assistance
The human has found the critically injured casualty.
His current goal is to bring the critically injured casualty to the medical room.
The robot doesn’t know this. It is searching for casualties in the other region.

## Slide 39: Use Case
How the robot provides proactive assistance
When the human enters into the field of view of the cameras, his actions are detected.
The robot recognizes that the critically injured casualty has been found and removes this goal from the goal set.
The robot realizes that bringing the medical kit to the human would achieve a better utility for the team.

## Slide 40: Use Case
How the robot provides proactive assistance
The robot recognizes that the critically injured casualty has been found and removes this goal from the goal set.
If the human chose to inform the robot about his goal, it could have done this directly (active support).
The robot realizes that bringing the medical kit to the human would achieve a better utility for the team.

## Slide 41: Use Case
How the robot provides proactive assistance
The robot realizes that bringing the medical kit to the human would achieve a better utility for the team.
If the lightly injured casualty was found instead, the robot would have decided to continue its search

## Slide 42: Use Case
How the robot provides proactive assistance
The robot realizes that bringing the medical kit to the human would achieve a better utility for the team.
If the lightly injured casualty was found but the critically injured casualty has already been treated, the robot would still help the human fetch the medical kit.

## Slide 43: Use Case
How the robot provides proactive assistance
Having computed its current goal, the robot generates a plan to achieve it using its automated planning component.

## Slide 44: Evaluation Criterion
Robot with and without proactive support ability.
– Hypothesis 1 –
  Robot with PS enables more effective teaming (e.g., less communication and more efficiency).
– Hypothesis 2 –
  Robot with PS increases human mental workload
Hypothesis for effectiveness of Proactive Support

## Slide 45
Objective Performance
Overall Task Performance
SIGNIFICANTLY
DIFFERENT
Cognitive Load
Total time taken for the team to find and treat the critically injured casualty
Total time taken for the team to finish the entire task
# Human stopped ROB from executing its current goal
# Subject had goal conflicts with ROB
# Human received goal updates from ROB
# Subject informing his goal to ROB
# Correct puzzles
Inconsistent with H2

## Slide 48: Subjective Likert Scale Questionnaire

## Slide 49
Subjective Performance
Mental Workload
Situation Awareness
Complacency
Ease of working with ROB
Participants workload to interact with ROB
Whether the subject felt that he/she had enough information to determine what the next goal should be
Comfort and ease of teaming
Consistent with H2
PS does not reduce SA much
Consistent with objective measures
How subject felt about their performance in the task
Notes: Updated

## Slide 50
Subjective Performance
Immediacy
Likability
Trust
How much the subject considered the simulated task as a realistic USAR task
How useful the participant felt about ROB as a teammate
Ease and comfort
Interaction between participant and ROB was effective?
Perceived effectiveness
ROB’s trustworthiness with the assignments
Effectiveness
Consistent with H1
Improvability
How much ROB could be improved ?
Balanced workload?
ROB’s trustworthiness with the updates during the task
ROB sometimes performed unexpectedly?
Notes: Updated

## Slide 52: Summary of Study 2 *
Results are mostly consistent with the hypotheses.
Subjects had positive feelings towards PS capabilities
  Seems to suggest that intelligent robots with a PS ability may be used and accepted in various settings
  The increased mental workload does not overwhelm the humans.
More investigations need to be conducted in scenarios with information asymmetry and human cognitive load.
Generally positive attitude towards Proactive Support
* “A Human Factors Analysis of Proactive Assistance in Human-robot Teaming” Yu (Tony) Zhang, Vignesh Narayanan, Tathagata Chakraborty & Subbarao Kambhampati. IROS 2015.

## Slide 53: Conclusions
Results of both the studies are mostly consistent with the hypotheses.
Subjects had positive feelings towards peer-to-peer (P2P) team* and proactive support (PS)** capabilities in general.
No significant increase in mental workload (for both P2P and PS team).
No significant decrease in situation awareness (for both P2P and PS team).
* “Automated Planning for Peer-to-peer Teaming and its Evaluation in Remote Human-Robot Interaction ” Vignesh Narayanan, Yu Zhang, Nathaniel Mendoza and Subbarao Kambhampati. 10th ACM/IEEE Intl. Conf on Human Robot Interaction (HRI), 2015.
** “A Human Factors Analysis of Proactive Assistance in Human-robot Teaming” Yu (Tony) Zhang, Vignesh Narayanan, Tathagata Chakraborty & Subbarao Kambhampati. IROS 2015.

## Slide 54: Thank you 